## Slide 1: Literature Review on Wearable/Mountable Robots for Positioning US Scanners
RAYAN HASSAN
UNIVERSITY OF PITTSBURGH
SUMMER UNDERGRADUATE RESEARCH PROGRAM (SRUP)
CUHK SUPERVISOR: PROF. HONGLIANG REN
DEPARTMENT OF ELECTRONIC ENGINEERING

## Slide 2: Content
Overview on Ultrasound (US) Principles
  Sound waves propagation
  Sound waves interactions with tissues
  Image resolution
  Transducers
Robotic Systems for US Scanning
  Mountable robots
  Wearable robots
  Soft robotics
Applications of Robots in US
  Human assisted systems
  Autonomous systems
Localization of Targeted Areas for US
  Review on convolutional neural networks (CNN)
  AI algorithms for US procedures

## Slide 3: Overview on Ultrasound Principles
Sound waves propagation
  Propagation: quick in dense material; slow in compressible material
  In soft tissues velocity of waves is constant
Sound waves interactions with tissues
  Reflection upon hitting a surface with different density
  The larger the difference the more echoes are reflected back
  Refraction: percentage of waves get through the surface tissue
  Other interactions include attenuation, interference, etc.
Image resolution
  Axial, lateral, spatial and temporal resolution
Transducers
  Operates by changing piezoelectric crystal’s shape in response to an electric field
  Wave sent with a centre frequency
  Wave decomposed into harmonic frequencies after hitting tissues
Fig.1 Difference between axial and lateral resolution shown in a US image

## Slide 4: Robotic Systems for US Scanning
Mountable robots
  Handle probe and position in optimal way
  Generation of 3D images
Wearable robots
  No risk caused by patient’s movement
  Brain simulation
Fig.2 KUKA LBR Med robotic arm Fig.3 Prototype of wearable robot for
transcranial US applications
Soft robotics
  Robots made out of soft materials
  Allow flexibility and compliance
    Fig.4 Attachable soft robot
  Origami devices: made out of flat composite sheets
  Limitless options for robotic designs

## Slide 5: Applications of Robots in US
Human assisted systems
  Teleoperation: operation of machine remotely
  System consists of robot that handles the probe (patient’s side) and screen with remote probe (doctor’s side)
  Fig.5 MELODY robotic system: example of remote US scanning
Autonomous systems
  Reduce human intervention
  Three main notions: 3D image reconstruction, trajectory planning and probe positioning, and image quality optimization

## Slide 6: Localization of Targeted Areas for US
Review on CNN
Convolution
ReLU
Pooling layer
S
O
F
T
M
A
X
1 Convolutional Layer
Fully Connected Layer
AI algorithms for US procedures
  Accurate localization of area of interest
  Helps predict the right area to scan
  Helps with other applications like drug delivery or tumour/infection detection

## Slide 7: References
Fig.1: Resolution. Radiology Key. (2016, March 10). Retrieved August 13, 2022, from https://radiologykey.com/resolution/
Fig.2: Unger, Michael, Berger, Johann, Gerold, Bjoern and Melzer, Andreas. "Robot-assisted Ultrasound-guided Tracking of Anatomical Structures for the Application of Focused Ultrasound" Current Directions in Biomedical Engineering, vol. 6, no. 3, 2020, pp. 123-126. https://doi.org/10.1515/cdbme-2020-3032
Fig.3: Kim, Joonwoo & Lee, Sungon. (2016). Development of a Wearable Robotic Positioning System for Noninvasive Transcranial Focused Ultrasound Stimulation. IEEE/ASME Transactions on Mechatronics. 21. 1-1. 10.1109/TMECH.2016.2580500.
Fig.4: H. Ren, X. Gu and K. L. Tan, "Human-compliant body-attached soft robots towards automatic cooperative ultrasound imaging," 2016 IEEE 20th International Conference on Computer Supported Cooperative Work in Design (CSCWD), 2016, pp. 653-658, doi: 10.1109/CSCWD.2016.7566066.
Fig.5: Melody, a remote, robotic ultrasound solution. AdEchoTech. (n.d.). Retrieved August 13, 2022, from https://www.adechotech.com/products/